## Slide 1: MONARCH BOARD & ITS PHOTOSENSORS
Viet M Bui, Bobby Schulz, Tyler Fulghum & Andy Wickert
DEVELOPMENT OF A BETTER SOLAR RADIATION INSTRUMENT

## Slide 2: INTRODUCTION
Sunlight
Electromagnetic radiation emitted by the Sun
Interact with our atmosphere
  Absorbed
  Scattered
  Reflected
Solar Irradiance and Solar UV Field Measurements, AVENTES
SOLAR RADIATION

## Slide 3: INTRODUCTION
Earth receives energy from solar radiation
  Critical to climate system, water cycle, life, etc.
Bush, Elizabeth & Loder, John & James, Thomas & Mortsch, Linda & Cohen, Stewart. (2014). An Overview of Canada's Changing Climate.
SOLAR RADIATION

## Slide 4: INTRODUCTION
Want to capture a wide range of spectrum UV to IR regions
Pyranometer is typically used to measure this range
Electromagnetic Wave Spectrum by Horst Frank is licensed CC-BY-SA 4.0 International
SPECTRUM

## Slide 5: INTRODUCTION
We will use the blackbody as the comparison with the two devices that we are going to setup and measure.
Credit: Nick84 [CC BY-SA 3.0] via Wikimedia Commons

## Slide 6: INTRODUCTION
The Boxcar function = the response across spectrum
Graph by Arthurcala

## Slide 7: INTRODUCTION
Industry standard (Kipp&Zonen CMP3) Thermopile Pyranometer
  Calibrated by hand
  Very expensive
  Not easily scalable for mass production and accessibility beyond the PV industry
We want to create an instrument
  Using different sensors (photodiodes)
  Photodiodes are mass produced with industrial purposes
  Use it as the high-quality environmental sensors
PROBLEM

## Slide 8: INTRODUCTION
To measure energy balance on glacier
Photosynthetically active radiation
General weather station
APPLICATION
Deployed station location near Perito Moreno Glacier, Argentina

## Slide 9: INTRODUCTION
HARDWARE
Monarch Board next to a US quarter

## Slide 10: INTRODUCTION
Spectral bandwidth~: 350 -> 1070 nm
HARDWARE
PHOTOSENSORS
INFRARED SHORTWAVE
CODE NAME: IR_SW
DIGITKEY: VEMD1060X01CT-ND
TYPE: PIN Photodiode
PIN photodiode cross-section, teamwavelength.com
Notes: APPLICATIONS • High speed photo detector • Small signal detection • Proximity sensors

## Slide 11: INTRODUCTION
Spectral bandwidth~: 800 -> 1700 nm
Near IR detection because of different material
  Indium Gallium Arsenide Photodiode
Overlapping with IR_SW
HARDWARE
PHOTOSENSORS
INFRARED MIDWAVE
CODE NAME: IR_MW
DIGITKEY: SD003-151-001CT-ND
TYPE: InGaAs Photodiode
Notes: APLICATIONS  Industrial Sensing  Security  Communication  Medical

## Slide 12: INTRODUCTION
Peak at 330 and 365 nm
Compact digital circuit:
  Photodiode
  Amplifiers
  Communication: I2C 16 bits
HARDWARE
PHOTOSENSORS
ULTRA-VIOLET
A
CODE NAME: UVA, UVB
DIGITKEY: VEML6075CT-ND
TYPE: ANALOG/DIGITAL CIRCUIT
B
Notes: Application: handheld device, medical instrument (skin cancer related)

## Slide 13: INTRODUCTION
Spectral bandwidth~: 400 -> 700 nm (filtered), 100 ->900 nm (broad)
High accuracy ambient light sensor
Measured in Lux
Compact digital circuit:
  Photodiode
  Amplifiers
  Communication: I2C 16 bits
HARDWARE
PHOTOSENSORS
WHITE
Broad
CODE NAME: WhiteBroad, WhiteFil
DIGITKEY: VEML6030-GS15CT-ND
TYPE: ANALOG/DIGITAL CIRCUIT
Filtered
Notes: Application: handheld device, medical instrument (skin cancer related)

## Slide 14: INTRODUCTION
HARDWARE
SPECTRAL RESPONSE

## Slide 15: INTRODUCTION
HARDWARE
COMPARISON

## Slide 16: METHODOLOGY
Using Zipp & Zonen CMP3 Pyranometer (industry standard) to compare how well Monarch board data correlate
The linear correlation:
  We are measuring numbers different from CMP3
  See how well we approximate the broad-band thermopile radiometer and not just reproducing it.
Could use the linear correlation to create transform function to output number to be as close to the industry standard

## Slide 17: METHODOLOGY
Margay Logger
CMP3
Monarch
SETUP

## Slide 18: RESULTS
JUNE 7-JULY 5, 2023, DATA
WILDFIRE SIGNATURE
OCT 10-13, 2024, DATA
HARDWARE ISSUE
CONDENSATION
MONARCH HOUSING
NOV, 2024, DATA

## Slide 19: RESULTS
JUNE 7-JULY 5, 2023, DATA
Data measured from Monarch Board plotted with Pyranometer value from CMP3 in x axis

## Slide 20: RESULTS
JUNE 7-JULY 5, 2023, DATA

## Slide 21: RESULTS
Orange Hue of Minneapolis’s skyline June 15
What does this tell us about the event on June 14?
Andy Wickert
WILDFIRE SIGNATURE
JUNE 7-JULY 5, 2023, DATA

## Slide 22: RESULTS
WILDFIRE SIGNATURE
Smoke event of June 14 2023, reached “Very Unhealthy” in Air Quality Index, MN DNR
JUNE 7-JULY 5, 2023

## Slide 23: RESULTS
IR_SW and IR_MW registered low numbers during mid day, could explain why the IR ranging so far down from the linear expectation correlated line?
WILDFIRE SIGNATURE
JUNE 7-JULY 5, 2023

## Slide 24: RESULTS
Relatively sunny condition
WILDFIRE SIGNATURE
JUNE 7-JULY 5, 2023

## Slide 25: RESULTS
A lot of overcast cloud
WILDFIRE SIGNATURE
JUNE 7-JULY 5, 2023

## Slide 26: RESULTS
WILDFIRE SIGNATURE
JUNE 7-JULY 5, 2023

## Slide 27: RESULTS
WILDFIRE SIGNATURE
JUNE 7-JULY 5, 2023

## Slide 28: RESULTS
WILDFIRE SIGNATURE
* UVB for x axis
! White Filtered for x axis
*
*
*
*
*
*
!
!
!
JUNE 7-JULY 5, 2023

## Slide 29: RESULTS
WILDFIRE SIGNATURE
* UVB for x axis
! White Filtered for x axis
*
*
*
*
*
*
!
!
!
JUNE 7-JULY 5, 2023
…In progress: Ratio comparison of the sensors between sunny, cloudy, smoke plots on the same time scale….

## Slide 30: RESULTS
Not far after June 14 beginning on the 19th the battery level of the instrument reaching < 3.5V
Margay logger operates >= 3.5V
Condensation happened  board corrosion
Could not look further into the high-quality data beyond the 19th
WILDFIRE SIGNATURE
JUNE 7-JULY 5, 2023

## Slide 31: RESULTS
Because the layer of Teflon that filter and protect the board was pealed off possibility from the winter to spring transition.
The old board cannot be read and new board needed for the 2024 test.
OCT 10-13, 2024, DATA

## Slide 32: RESULTS
OCT 10-13, 2023, DATA
Data measured from Monarch Board plotted with Pyranometer value from CMP3 in x axis

## Slide 33: RESULTS
2 ways to look at this dataset
  Could be from the hardware itself where the I2C interface on the Vis board has problem in communication (bad soldering from the manufacture that we contracted?)
  Could coming from the container itself (Monarch’s housing)
OCT 10-13, 2024, DATA

## Slide 34: RESULTS
Identified problem:
  Whole batch of Monarch has issue with an I2C component was not securely soldered because it was a heat sink.
    Did not fully reflow in oven
  This issue will take longer to resolve.
Solution: use the hand-soldered board used for the Ecuador project.
OCT 10-13, 2024, DATA

## Slide 35: RESULTS
NOV 2024, DATA
Data measured Between 16 and 17 November

## Slide 36: RESULTS
NOV 2024, DATA
Data measured on 17 November because it is with sunny condition

## Slide 37: RESULTS
NOV 2024, DATA
Data measured on 17 November because it is with sunny condition

## Slide 38: RESULTS
NOV 2024, DATA
2023 Data

## Slide 39: RESULTS
NOV 2024, DATA
2023 Data

## Slide 40: RESULTS
NOV 2024, DATA
Desiccant inside Margay Housing
Humidity and condensation inside the housing resolved by new batch of desiccant
CONDENSATION
Desiccant inside Monarch Housing
Exterior remains the same issue with condensation in early mornings

## Slide 41: RESULTS
NOV 2024, DATA
More control environment with the housing is needed
Redesign the flat top cover
MONARCH HOUSING

## Slide 42: NEXT STEP
Continue looking at the new set of data from the hand soldered board
Averaging RGB values from the set of photos taken by the camera for Nov data
Redesign and Improve the housing for Monarch…
  Host engineering design event: Senior design team in MechE

## Slide 43: NEXT STEP
CURRENT
NEW?

## Slide 44: QUESTION?
FOR THE DEVELOPMENT OF A BETTER SOLAR RADIATION INSTRUMENT
Thanks a million, to Bobby Schulz, Uma Arshani and Andy Wickert